## Slide 1: The Carbon Farming Initiative and Agricultural Emissions
This presentation was prepared by the University of Melbourne for the Regional Landcare Facilitator training funded through the Australian Government’s Carbon Farming Initiative Communications Program

## Slide 2: This presentation provides background information on methane emissions, their global potential and explains methanogenesis
PART 5: METHANE FROM ANIMAL PRODUCTION
Notes: This section takes 15 minutes

## Slide 3: Methane from animal production
Content
  Introduction and background to methane emissions
  Global warming potential
  Methanogenesis in the rumen
  Methanogenesis in waste management systems
  Factors affecting methanogenesis

## Slide 4: Methane from animal production
Global Trends in Atmospheric Methane
IPCC 2007

## Slide 5: Methane from animal production
Australian Trends in Atmospheric Methane
CSIRO 2011

## Slide 6: Methane from animal production
Unexpected rise in global methane concentrations from 2007
Mascarelli (2009)

## Slide 7: Methane from animal production
DCCEE 2011
Chart: Gt CO2e
| Dairy Cattle | Non-Dairy Cattle | Alpacas | Deer | Ostriches and Emus | Buffalo | Sheep | Goats | Camels and Llamas | Horses | Donkeys | Swine
 | 6603.97 | 37857.84 | 1.59 | 11.66 | 30.02 | 9.65 | 10547.01 | 72.78 | 3.02 | 97.61 | 0.33 | 1203.04
Australian Methane Emissions

## Slide 8: Methane from animal production
Global warming potential
  Shorter lifetime in atmosphere
    8 to 12 years
  Concentrations
    Pre-industrial - 700 ppb
    Current - 1745 ppb
  High GWP
    72 x CO2 on a 20 year time horizon
    21 x CO2 on a 100 year time horizon (AR2 – DCCEE)
    25 x CO2 on a 100 year time horizon (AR4)
IPCC 2007

## Slide 9: Methane from animal production
Ruminants (cows, sheep)
  95% breathed and eructated
  5% from flatus
Non-Ruminants (pigs, poultry, horses)
  Mainly from flatus
  Horses, rabbits
    Extended caecum for microbial digestion
Effluent ponds
  Anaerobic ponds = more methane
Eckard 2011
Chart: 
| Enteric Fermentation (64.59) | Manure Management (3.91%) | Rice Cultivation (0.05%) | Agricultural Soils (16.75%) | Prescribed Burning of Savannas (14.33%) | Field Burning of Agricultural Residues (0.18%)
Gg (1,000 Tonnes) | 54736.47 | 3315.92 | 46.28 | 14191.19 | 12146.64 | 309.12

## Slide 10: Methane from animal production
Microbes in the microbial digestion
  Bacteria, protozoa, fungi, archaea, and viruses
    40-60% bacteria, protozoa
    5-10% fungi
    3% Archaea (methanogens)
      Normal component of the rumen
      Many species yet to be identified!
      Eckard 2011

## Slide 11: Methane from animal production
Methanogensis
  A form of anaerobic respiration
    4H2 +CO2→CH4 +2H2O
  Uses H2 to reduce CO2 to form CH4
  Volatile Fatty Acid (VFA) production produces H2
    BUT H2 can also affect VFA production
  Interspecies hydrogen transfer
    From bacteria and protozoa to methanogens
      Klieve & Ouwerkerk 2007; Attwood & McSweeney 2009; McAllister & Newbold 2009

## Slide 12: Methane from animal production
Volatile Fatty Acid production
  More propionate, less H2, thus less CH4
  More butyrate and acetate, more H2, thus more CH4
Jansen 2010

## Slide 13: Methane from animal production
Waste management systems
  Piggery > Dairy > Poultry
Chart: Gg CO2e
| Dairy Cattle | Non-Dairy Cattle | Alpacas | Deer | Ostriches and Emus | Buffalo | Sheep | Goats | Camels and Llamas | Horses | Donkeys | Swine
Animal | 6129.62 | 37765.28 | 1.59 | 11.65 | 29.99 | 9.64 | 10544.21 | 72.74 | 3.02 | 97.46 | 0.33 | 70.94
Waste | 474.35 | 92.56 | 0 | 0.01 | 0.03 | 0.01 | 2.8 | 0.04 | 0 | 0.15 | 0 | 1132.1
DCCEE 2011

## Slide 14: Methane from animal production
Waste management systems
  % of total on farm CH4 from waste management
    7% of Dairy farm
    95% of Piggery
DCCEE 2011
Chart: 
| Enteric Fermentation (64.59) | Manure Management (3.91%) | Rice Cultivation (0.05%) | Agricultural Soils (16.75%) | Prescribed Burning of Savannas (14.33%) | Field Burning of Agricultural Residues (0.18%)
Gg (1,000 Tonnes) | 54736.47 | 3315.92 | 46.28 | 14191.19 | 12146.64 | 309.12

## Slide 15: Methane from animal production
Less CH4
  Faster rumen passage
  More O2
  Less methanogens
  Less H2
  Carbon
  Lower temperature
More CH4
  Slower rumen rate
  Less O2
  More methanogens
  More H2
  Acid rumen pH
  Higher temperature
Factors affecting methanogenesis
Eckard 2011

## Slide 16: Methane from animal production
Animal Class | Methane (kg/year) | MJ CH4 lost /hd/day | Effective annual grazing days lost | Potential km driven in 6-cylinder car
Mature ewe | 6 to 10 | 0.9 to 1.5 | 26 to 43 | 54 to 90
Beef steer | 50 to 90 | 7.6 to 13.6 | 33 to 60 | 450 to 800
Dairy cow | 90 to 146 | 13.6 to 22.1 | 25 to 40 | 800 to 1350
Largest inefficiency in animal production
  Methane energy content - 55.22 MJ/kg
  6 to 10% of GEI lost as CH4
But: we cannot abate 100%
Eckard, Grainger & de Klein 2010